## Slide 1
Andrea Bottin
a.bottin@otbioelettronica.it
BIOPOTENTIALS, EMG DETECTION
AND PROCESSING

## Slide 2
TOPICS
OT BIOELETTRONICA
BIOPOTENTIALS
EMG GENERATION AND DETECTION
EMG PROCESSING
APPLICATIONS

## Slide 3
TOPICS
OT BIOELETTRONICA
BIOPOTENTIALS
EMG GENERATION AND DETECTION
EMG PROCESSING
APPLICATIONS

## Slide 4
OT BIOELETTRONICA PRODUCTS
Quattrocento
384ch
Sessantaquattro+
64ch
MuoviPro 4x32ch
Muovi+Pro 2x32ch
Novecento+ 960ch
Available since Jne 2024

## Slide 5
OT BIOELETTRONICA ELECTRODE ARRAYS

## Slide 6
OT BIOELETTRONICA ELECTRODE MATRICES

## Slide 7
OT BIOELETTRONICA DYNAMOMETERS

## Slide 8
WHERE WE ARE

## Slide 9
WHO WE ARE

## Slide 10
CUSTOMERS AND COLLABORATIONS

## Slide 11
TOPICS
OT BIOELETTRONICA
BIOPOTENTIALS
EMG GENERATION AND DETECTION
EMG PROCESSING
APPLICATIONS

## Slide 12
The body produces many different types of biopotentials.
Sources of potentials:
- skeletal muscle (EMG)
- brain (EEG)
- heart (ECG)
eye (EOG)
- stomach (EGG)
The electrical activity can be recorded on the surface of the skin.
BIOPOTENTIALS

## Slide 13
ELECTROCARDIOGRAM - ECG
Most diffused and used biopotential
Known since 1842
Amplitude on the skin: 1 ÷ 5 mV
Bandwidth: 0.5 ÷ 150 Hz
Channels: 1 ÷ 9

## Slide 14
ELECTROENCEPHALOGRAM - EEG
Known since 1929
Amplitude on the scalp: 5 ÷ 200 µV
Bandwidth: 0.5 ÷ 100 Hz
Channels: up to 256

## Slide 15
ELECTROENCEPHALOGRAM - EEG
Name | Frequency | Subject condition
Alpha Rhythm | 8 – 13 Hz | Quiet resting activity, eyes closed
Beta Rhythm | 13 – 22 Hz | Awake, attentive state
Delta Rhythm | 0.5 – 4 Hz | Stressful activity or brain disorders
Theta Rhythm | 4 – 8 Hz | Deep sleep, brain disorders
Gamma Rhythm | 22 – 100 Hz | Neural oscillation, transcendental mental states

## Slide 16
SURFACE ELECTROMYOGRAM - sEMG
Known since 1966
Amplitude on the skin: 5 µV ÷ 10 mV
Bandwidth: 10 ÷ 500 Hz
Channels: up to 400

## Slide 17
INTRAMUSCULAR ELECTROMYOGRAM - iEMG
Known since 1938
Amplitude: 1 ÷ 5 mV
Bandwidth: 100 ÷ 5000 Hz
Channels: 1 ÷ 4

## Slide 18
TOPICS
OT BIOELETTRONICA
BIOPOTENTIALS
EMG GENERATION AND DETECTION
EMG PROCESSING
APPLICATIONS

## Slide 19: MOTOR UNITS
Notes: Electrical event to a mechanical event

## Slide 20
Motor cortex
α motor neurons
MU_1
Innervation zone
Conduction velocity: 4 m/s
MU_2
Conduction velocity: 6 m/s
MOTOR UNITS ACTION POTENTIAL

## Slide 21
Skin
MU_1
MU_2
MU_3
Innervation zone

Tendon
Filter
Electrode

MUAPs

MUAPs

RECORDING EMG FROM THE SKIN SURFACE

## Slide 22: Intramuscular EMG - (iEMG)
100 ms
100 ms
Surface EMG - (sEMG)
sEMG vs iEMG

## Slide 23
sEMG
iEMG
3.32
3.34
3.36
3.38
3.4
3.42
Time (s)
sEMG vs iEMG

## Slide 24
INTRAMUSCULAR NEEDLE ELECTRODES
The different types of needle electrodes have different recording
volumes covering different portions of a motor unit territory.

## Slide 25
INTRAMUSCULAR WIRE ELECTRODES
Thin wire inserted with a needle
After insertion the needle can be removed
Only the tip of the wire is exposed
Allows the detection during movements
Connection Pad
Array
Guiding Filament
Insertion Needle
Electrode Line
Multipoint intramuscular detection
Developed in Germany at UMG

## Slide 26
BIPOLAR SURFACE EMG DETECTION

## Slide 27
BIPOLAR PLACEMENT
Wrong Bipolar Placement
Proper Bipolar placement

## Slide 28
Monopolar
Bipolar or single differential
Linear electrode array
Second electrode at “zero” potential
MULTICHANNEL sEMG DETECTION MODES

## Slide 29
Channel with smaller amplitude, possibly near or over the innervation zone.
Three SD channels provide some additional information
With 7 channels we begin to see patterns that might be the “signatures” of motor units
tendon
tendon
Innervation Zone
SIGNATURES OF MOTOR UNITS

## Slide 30
DRY ARRAYS
Suitable only for short term acquisition and for the location of the best position on the muscle
ELECTRODE ARRAYS
ADHESIVE ARRAY
Suitable for long term acquisition and for dynamic contractions

## Slide 31
Mylar support layer
Silver deposed with serigraphic process
Siliconic paper for the insulation of traks
Holes for the gel insertion
Silver chloride electrodes
Holes for the exposure of electrodes
Skin
ADHESIVE ELECTRODE ARRAY AND GRIDS PLACEMENT
Double adhesive foam
Electrode support

## Slide 32
2D electrode array (HD-sEMG)
Monopolar
Bipolar
Linear electrode array
HIGH DENSITY SURFACE EMG (HD-sEMG)

## Slide 33
ELECTRODE MATRICES

## Slide 34
iEMG
sEMG
Non-Invasive (no pain)
Exact estimation of conduction velocity
Detection area
No cross-talk
Discharge rate estimation
Estimation of MU recruitment thresholds
HD-sEMG
Easy to perform
No danger
(no risk of infections)
iEMG VS sEMG VS HD-sEMG

## Slide 35
TOPICS
OT BIOELETTRONICA
BIOPOTENTIALS
EMG GENERATION AND DETECTION
EMG PROCESSING
APPLICATIONS

## Slide 36
HOW EMG CHANGE
MUSCLE FATIGUE
Relationship EMG-Force
Relationship EMG-Fatigue

## Slide 37
FREQUENCY CONTENT

## Slide 38
MANIFESTATIONS OF MUSCLE FATIGUE
MUSCLE FATIGUE
FREQUENCY
TIME
A.U.
A.U.

## Slide 39
CONDUCTION VELOCITY - CV
Time
Space
V = S/t
4cm
10ms

## Slide 40
CONDUCTION VELOCITY CHANGES WITH FATIGUE
Time
Space
4cm
10ms
4cm
18ms
4cm
15ms
4cm
12ms

## Slide 41
EMG VARIABLES DURING MUSCLE FATIGUE
30
40
50
60
70
Torque
(%MVC)
MNF
(Hz)
CV
(m/s)
ARV
(mV)
Fractal
Dimension
10
20
Isometric contraction 70%±5% MVC
Decrease of muscle fiber conduction velocity
Decrease of spectral frequency content
Muscle fatigue
Increase of EMG amplitude
(MUAP slow down)
Decrease of FD
(MU synchronization)
Endurance time
4
5
6
40
60
80
0.1
0.2
0.3
1.55
1.54
1.53

## Slide 42
ACTIVATION MAP

## Slide 43
EMG DECOMPOSITION
Electrode grid
Surface EMG signals
summation of all active MUs
MUs Reppresentation on each electrode
Firing patterns
α-motoneurons

## Slide 44
EMG DECOMPOSITION RESULT

## Slide 45
EMG DECOMPOSITION RESULT

## Slide 46
TOPICS
OT BIOELETTRONICA
BIOPOTENTIALS
EMG GENERATION AND DETECTION
EMG PROCESSING
APPLICATIONS

## Slide 47
AMYO PROJECT
Advanced Myoelectric Control of Prosthetic Systems
European Project involving Ottobock, OT Bioelettronica, UM Goettingen, TU Berlin
Detection of EMG from the forearm to drive a multiple degree of freedom prostetic hand in a new intuitive way

## Slide 48
TARGETED MUSCLE REINNERVATION

## Slide 49
MuoviPro
4 x 32 sEMG channel device with Wi-Fi communication

## Slide 50
MuoviPro
2 x 64 sEMG channel device with Wi-Fi communication

## Slide 51
MuoviPro & Muovi+Pro options
muovi+
due+
SyncStation
muovi
muovi
muovi
muovi
WiFi
& Sync pulses
muovi+
due+
due+
32
EMG/EEG
64
EMG/EEG
32
EMG/EEG
32 EMG/EEG
32 EMG/EEG
64
EMG/EEG
2 EMG
2 EMG
2 EMG
Up to 8
3 AUX input
±5 V
Load cell input
Sync output
Ethernet
4 EMG
4 EMG
quattro+
quattro+
optional

## Slide 52
KINELOCK

## Slide 53
BRUXOFF – BRUXISM DIAGNOSIS

## Slide 54
NOD – THREE FUNCIONS FOR PHYSIOTHERAPISTS
Dynamometer The Hand-Held Dynamometer is a portable device used for muscle strength measurement
Force Biofeedback The force biofeedback is the technique of providing a real-time information of the force produced by the neuromuscular contraction.
Algometer The algometer is a clinal and research tool for the assessment of the musculoskeletal pain.

## Slide 55
THANK YOU